## Slide 1: Ειδικά Θέματα Αρχιτεκτονικής και Προγραμματισμού Μικροεπεξεργαστών
Εργαστήριο
Διδάσκων: Βαρτζιώτης Φώτιος
Τμήμα Πληροφορικής και Τηλεπικοινωνιών

## Slide 2: Introduction
What is QtSpim?
  a simulator that runs assembly programs for MIPS R2000/R3000 RISC computers
Resources
  http://spimsimulator.sourceforge.net/
  Computer Organization & Design: The Hardware/Software Interface”, by Patterson and Hennessy: Chapter 3 and Appendix A.9-10
What does QtSpim do?
  reads MIPS assembly language files and translates to machine language
  executes the machine language instructions
  shows contents of registers and memory
  works as a debugger (supports break-points and single-stepping)
  provides basic OS-like services, like simple I/O

## Slide 3: Learning MIPS & QtSpim
MIPS assembly is a low-level programming language
The best way to learn any programming language is from live code
We will get you started by going through a few example programs and explaining the key concepts
We will not try to teach you the syntax line-by-line: pick up what you need from the book and on-line tutorials
Tip: Start by copying existing programs and modifying them incrementally making sure you understand the behavior at each step
Tip: The best way to understand and remember a construct or keyword is to experiment with it in code, not by reading about it

## Slide 4: QtSpim Installation
Windows Installation
  download the .msi file from https://sourceforge.net/projects/spimsimulator/files/ and save it on your machine. For your convenience a copy is kept locally at the class website
  Double click to install..

## Slide 5: QtSpim Windows Interface
Registers window
  shows the values of all registers in the MIPS CPU and FPU
Data segment window
  shows the data loaded into the program’s memory and the data of the program’s stack
Text segment window
  shows assembly instructions & corresponding machine code
Messages window
  shows :QtSpim messages
Separate console window appears for I/O

## Slide 6: Using :QtSpim
Loading source file
  Use File -> Open menu
Simulation
  Simulator -> Go : run loaded program
    Click the OK button in the Run Parameters pop-up window if the starting address value is “0x00400000”
  Simulator -> Break : stop execution
  Simulator -> Clear Registers and Reinitialize : clean-up before new run
Important!!

## Slide 7: Using QtSpim
  Simulator -> Reload : load file again after editing
  Simulator -> Single Step or Multiple Step : stepping to debug
  Simulator -> Breakpoints : set breakpoints
Notes:
  text segment window of QtSpim shows assembly and corresponding machine code
    pseudo-instructions each expand to more than one machine instruction
  if Delayed Branches is checked in Simulator -> Settings (tab MIPS)… then statementx will execute before control jumps to L1 in following code – to avoid insert nop before statementx:
nop
jal L1
statementx
…
L1: …

## Slide 8: QtSpim Example Program: add2numbersProg1.asm
## Program adds 10 and 11
.text # text section
.globl main # call main by SPIM
main:
ori $8,$0,0xA # load “10" into register 8
ori $9,$0,0xB # load “11" into register 9
add $10,$8,$9 # add registers 8 and 9, put result
# in register 10

## Slide 9: MIPS Assembly Code Layout
Typical Program Layout
.text #code section
.globl main #starting point: must be global
main:
# user program code
.data #data section
# user program data

## Slide 10: MIPS Assembler Directives
Top-level Directives:
  .text
    indicates that following items are stored in the user text segment, typically instructions
  .data
    indicates that following data items are stored in the data segment
  .globl sym
    declare that symbol sym is global and can be referenced from other files

## Slide 11: QtSpim Example Program: add2numbersProg2.asm
# Program adds 10 and 20
.text # text section
.globl main # call main by SPIM
main:
la $t0, value # load address ‘value’ into $t0
lw $t1, 0($t0) # load word 0(value) into $t1
lw $t2, 4($t0) # load word 4(value) into $t2
add $t3, $t1, $t2 # add two numbers into $t3
sw $t3, 8($t0) # store word $t3 into 8($t0)
.data # data section
value: .word 10, 20, 0 # load data integers. Default data
# start address 0x10010000(= value)
Parse the
machine code
for these two
instructions!

## Slide 12: MIPS Memory Usage as viewed in QtSpim
reserved
0x00000000
0x00400000
0x10010000
0x7fffeffc
0x7fffffff
text segment
(instructions)
data segment
stack segment
reserved

## Slide 13: MIPS Assembler Directives
Common Data Definitions:
  .word w1, …, wn
    store n 32-bit quantities in successive memory words
  .half h1, …, hn
    store n 16-bit quantities in successive memory halfwords
  .byte b1, …, bn
    store n 8-bit quantities in successive memory bytes
  .ascii str
    store the string in memory but do not null-terminate it
      strings are represented in double-quotes “str”
      special characters, eg. \n, \t, follow C convention
  .asciiz str
    store the string in memory and null-terminate it

## Slide 14: MIPS Assembler Directives
Common Data Definitions:
  .float f1, …, fn
    store n floating point single precision numbers in successive memory locations
  .double d1, …, dn
    store n floating point double precision numbers in successive memory locations
  .space n
    reserves n successive bytes of space
  .align n
    align the next datum on a 2n byte boundary. For example, .align 2 aligns next value on a word boundary. .align 0 turns off automatic alignment of .half, .word, etc. till next .data directive

## Slide 15: QtSpim Example Program: storeWords.asm
## Program shows memory storage and access (big vs. little endian)
.data
here: .word 0xabc89725, 100
.byte 0, 1, 2, 3
.asciiz "Sample text"
there: .space 6
.byte 85
.align 2
.byte 32
.text
.globl main
main:
la $t0, here
lbu $t1, 0($t0)
lbu $t2, 1($t0)
lw $t3, 0($t0)
sw $t3, 36($t0)
sb $t3, 41($t0)
Word placement in memory is exactly same in
big or little endian – a copy is placed.
Byte placement in memory depends on if it is
big or little endian. In big-endian bytes in a
Word are counted from the byte 0 at the left
(most significant) to byte 3 at the right
(least significant); in little-endian it is the
other way around.
Word access (lw, sw) is exactly same in big or
little endian – it is a copy from register to
a memory word or vice versa.
Byte access depends on if it is big or little endian,
because bytes are counted 0 to 3 from left to right
in big-endian and counted 0 to 3 from right to
left in little-endian.
SPIM’s memory storage depends on the underlying
machine: Intel 80x86 processors are little-endian!

## Slide 16: QtSpim Example Program: swap2memoryWords.asm
## Program to swap two memory words
.data # load data
.word 7
.word 3
.text
.globl main
main:
lui $s0, 0x1001 # load data area start address 0x10010000
lw $s1, 0($s0)
lw $s2, 4($s0)
sw $s2, 0($s0)
sw $s1, 4($s0)

## Slide 17: QtSpim Example Program: branchJump.asm
## Nonsense program to show address calculations for
## branch and jump instructions
.text # text section
.globl main # call main by SPIM
# Nonsense code
# Load in SPIM to see the address calculations
main:
j label
add $0, $0, $0
beq $8, $9, label
add $0, $0, $0
add $0, $0, $0
add $0, $0, $0
add $0, $0, $0
label:
add $0, $0, $0

## Slide 18: QtSpim Example Program: procCallsProg2.asm
.text
.globl main
main:
la $a0, array
addi $a1, $0, 0
addi $sp, $sp, -4
sw $ra, 0($sp)
jal swap
lw $ra, 0($sp)
addi $sp, $sp, 4
jr $ra
# equivalent C code:
# swap(int v[], int k)
# {
# int temp;
# temp = v[k];
# v[k] = v[k+1];
# v[k+1] = temp;
# }
# swap contents of elements $a1
# and $a1 + 1 of the array that
# starts at $a0
swap: add $t1, $a1, $a1 add $t1, $t1, $t1
add $t1, $a0, $t1
lw $t0, 0($t1)
lw $t2, 4($t1)
sw $t2, 0($t1)
sw $t0, 4($t1)
jr $ra
.data
array: .word 5, 4, 3, 2, 1
## Procedure call to swap two array words
save return
address $ra
in stack
jump and
link to swap
restore
return
address
jump to $ra
load para-
meters for
swap

## Slide 19: MIPS: Software Conventions for Registers
0 zero constant 0
1 at reserved for assembler
2 v0 results from callee
3 v1 returned to caller
4 a0 arguments to callee
5 a1 from caller: caller saves
6 a2
7 a3
8 t0 temporary: caller saves
. . . (callee can clobber)
15 t7
16 s0 callee saves
. . . (caller can clobber)
23 s7
24 t8 temporary (cont’d)
25 t9
26 k0 reserved for OS kernel
27 k1
28 gp pointer to global area
29 sp stack pointer
30 fp frame pointer
31 ra return Address (HW):
caller saves

## Slide 20: QtSpim System Calls
System Calls (syscall)
  OS-like services
Method
  load system call code into register $v0 (see following table for codes)
  load arguments into registers $a0, …, $a3
  call system with QtSpim instruction syscall
  after call return value is in register $v0, or $f0 for floating point results

## Slide 21: SPIM System Call Codes
Service | Code (put in $v0) | Arguments | Result
print_int | 1 | $a0=integer | 
print_float | 2 | $f12=float | 
print_double | 3 | $f12=double | 
print_string | 4 | $a0=addr. of string | 
read_int | 5 |  | int in $v0
read_float | 6 |  | float in $f0
read_double | 7 |  | double in $f0
read_string | 8 | $a0=buffer, $a1=length | 
sbrk | 9 | $a0=amount | addr in $v0
exit | 10 |  | 

## Slide 22: QtSpim Example Program: systemCalls.asm
## Enter two integers in
## console window
## Sum is displayed
.text
.globl main
main:
la $t0, value
li $v0, 5
syscall
sw $v0, 0($t0)
li $v0, 5
syscall
sw $v0, 4($t0)
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 8($t0)
li $v0, 4
la $a0, msg1
syscall
li $v0, 1
move $a0, $t3
syscall
li $v0, 10
syscall
.data
value: .word 0, 0, 0
msg1: .asciiz “Sum = "
system call code
for read_int
result returned by call
argument to print_string call
system call code
for print_string
system call code
for print_int
argument to print_int call
system call code
for exit

## Slide 23: Conclusion & More
The code presented so far should get you started in writing your own MIPS assembly
Remember the only way to master the MIPS assembly language – in fact, any computer language – is to write lots and lots of code
For anyone aspiring to understand modern computer architecture it is extremely important to master MIPS assembly as all modern computers (since the mid-80’s) have been inspired by, if not based fully or partly on the MIPS instruction set architecture
To help those with high-level programming language (e.g., C) experience, in the remaining slides we show how to synthesize various high-level constructs in assembly…

## Slide 24: Synthesizing Control Statements (if, if-else)
if ( condition ) {
statements
}
beqz $t0, if_end_label
# MIPS code for the
# if-statements.
if_end_label:
if ( condition ) {
if-statements
} else {
else-statements
}
beqz $t0, if_else_label
# MIPS code for the
# if-statements.
j if_end_label
if_else_label:
# MIPS code for the
# else-statements
if_end_label:

## Slide 25: Synthesizing Control Statements (while)
while ( condition ) {
statements
}
while_start_label:
# MIPS code for the condition expression
beqz $t0, while_end_label
# MIPS code for the while-statements.
j while_start_label
while_end_label:

## Slide 26: Synthesizing Control Statements (do-while)
do {
statements
} while ( condition );
do_start_label:
# MIPS code for the do-statements.
do_cond_label:
# MIPS code for the condition expr:
beqz $t0, do_end_label
j do_start_label
do_end_label:

## Slide 27: Synthesizing Control Statements (for)
for ( init ; condition ; incr ) {
statements
}
# MIPS code for the init expression.
for_start_label:
# MIPS code for the condition expression
beqz $t0, for_end_label
# MIPS code for the for-statements.
for_incr_label:
# MIPS code for the incr expression.
j for_start_label
for_end_label:

## Slide 28: Synthesizing Control Statements (switch)
switch ( expr ) {
case const1:
statement1
case const2:
statement2
...
case constN:
statementN
default:
default-statement
}
# MIPS code to compute expr.
# Assume that this leaves the
# value in $t0
beq $t0, const1, switch_label_1
beq $t0, const2, switch_label_2
...
beq $t0, constN, switch_label_N
# If there is a default, then add
b switch_default
# Otherwise, add following lineinstead:
b switch_end_label

## Slide 29: Synthesizing Control Statements (switch), cont.
switch_label_1:
# MIPS code to compute statement1.
switch_label_2:
# MIPS code to compute statement2.
...
switch_label_N:
# MIPS code to compute statementN.
# If there's a default:
switch_default:
# MIPS code to compute default-statement.
switch_end_label:

## Slide 30: Array Address Calculation
Address calculation in assembler:
address of A [n] = address of A [0] + (n* sizeof (element of A))
# $t0 = address of start of A.
# $t1 = n.
mul $t2, $t1, 4 # compute offset from
# the start of the array
# assuming sizeof(element)=4
add $t2, $t0, $t2 # add the offset to the
# address of A [0].
# now $t2 = &A [n].
sw $t3, ($t2) # A [n] = whatever is in $t3.
lw $t3, ($t2) # $t3 = A [n].

## Slide 31: Short-Cut Expression Evaluation (and)
cond1 && cond2
# MIPS code to compute cond1.
# Assume that this leaves the value in $t0.
# If $t0 is zero, we're finished
# (and the result is FALSE).
beqz $t0, and_end
# MIPS code to compute cond2.
# Assume that this leaves the value in $t0.
and_end:

## Slide 32: Short-Cut Expression Evaluation (or)
cond1 || cond2
# MIPS code to compute cond1.
# Assume that this leaves the value in $t0.
# If $t0 is not zero, we're finished
# (and the result is TRUE).
bnez $t0, or_end
# MIPS code to compute cond2.
# Assume that this leaves the value in $t0.
or_end: