## Slide 1: Τηλεπικοινωνιακά Δίκτυα
ΠΜΣ Μηχανικών Ηλεκτρονικών Υπολογιστών και Δικτύων
Τμήμα Πληροφορικής & Τηλεπικοινωνιών – Πανεπιστήμιο Ιωαννίνων
Διδάσκοντες
Κωνσταντίνος Αγγέλης
Καθηγητής
Ανδρέας Τσορμπατζόγλου
Επίκουρος Καθηγητής

## Slide 2: 4. Channel estimation procedure
4.1 Channel characteristics estimation
In order to estimate the channel characteristics, we expand each transmitted and received signals in time and write into signal matrix columns K discrete samples in time.
The signals matrixes get K rows and as many columns as we have antennas, N or M.
In general a MIMO system involves multiple antennas at the transmitting end and multiple receivers at the receiving end.
Figure 4 show a general representation of a 3 x 3 general MIMO system.

## Slide 3: 4. Channel estimation procedure
4.1 Channel characteristics estimation
In order to determine the characteristic of the channel, both the transmitted signal X and the received signal Y have to be known.
If the transmitted and received signals are of the form:
If the channel transfer matrix Wc can be determined, then it means the transmitted signals can also be determined because the received signal Y is known.
We may write the expression between these vector signals as

## Slide 4: 4. Channel estimation procedure
4.1 Channel characteristics estimation
In order to determine the transmitted signals, the channel transfer matrix, Wc -1 have to be inverted and then multiplied with the received signal matrix Y.
The channel transfer matrix that we have to solve with the help of known training signal X and the received signal Y has the form

## Slide 5: 4. Channel estimation procedure
4.1 Channel characteristics estimation
The channel transfer matrix is calculated periodically with the help of the known training signals and remains constant over information transmission time. It is then recalculated when new information is being transmitted. The channel characteristics in equation (4.1.4) are defined for each signal path at discrete time instants 1,2,...K.
However, we need to derive Wc and this can be derived with the help of the transmitted signals X and the corresponding known received signals Y measured at the receiver.
Equation (4.1.4) expresses the channel matrix Wc which do not need to be a square matrix. Because, for example if we have a 4x4 MIMO system with 100 samples, we do not need to have a 100x100 channel matrix.
However, 5 samples can be transmitted from the four (4) antennas at a time. The next section explains the procedures required in order to estimate the channel transfer matrix Wc.

## Slide 6: 4. Channel estimation procedure
4.2 Channel identification algorithm
To model the transfer channel a common space matrix (orthonormal basis matrix Ux) is first generated and then used to map both the transmitted and received signals that vary in space (multiple antennas) and in time (samples in time).
This common orthonormal basis matrix is obtained by decomposing either the transmitted signal X or the received signal Y. Hence, MIMO channel problem can be solved using four step approach under a condition where there is no noise (N = 0) and if the transmitted signals are orthogonal.

## Slide 7: 4. Channel estimation procedure
4.2 Channel identification algorithm
These steps are summarized as follows:

## Slide 8: 4. Channel estimation procedure
4.2 Channel identification algorithm
Figure 5 shows the various steps required to model the transfer channel Wc.:
Reference to figure 5, it can deduce that the first principle is to map both the transmitted and the received signals with a common space matrix, the orthonormal basis vector.
The second process in figure 5 is to determine the Fourier coefficients of both the
transmitted and the received signals.
The final process is to model the transfer channel with the help of the Fourier confidents obtained.
It is important to explain in details the four listed steps for clear understanding.
The next section explains these four principles.

## Slide 9: 4. Channel estimation procedure
4.2.1 Orthonormal basis Ux estimation

## Slide 10: 4. Channel estimation procedure
4.2.2 Fourier coefficients of transmitted signal Wx

## Slide 11: 4. Channel estimation procedure
4.2.3 Fourier coefficients of training (received) signal Wy

## Slide 12: 4. Channel estimation procedure
4.2.4 Transfer Channel matrix estimation Wc
The orthonormal basis Ux plays an important role in determining the channel characteristics and therefore it is important to develop an algorithm to generate Ux. Not only to generate the orthonormal basis matrix but to illustrate the entire matrixes required to estimate the transfer channel.

## Slide 13: 5. Orthonormal space concept
5.1 Orthonormal basis of transmitted signal
Orthonormal basis is a coordination system where we can present as many dimensions as is the maximum number of antennas of the transmitted and received signals.
The main reason why we need the orthonormal base is to have a common coordinated system in order to combine the transmitted signal X and the received signal Y.
The number of dimension of the orthonormal base matrix depends on the maximum number of antennas at both the transmitted and the receiver end of the MIMO system.
It does not actually matter what kind of signal (X or Y) used in generating the orthonormal space but it is most convenient to use the transmitted training signal X which is defined to contain linearly independent column signals.

## Slide 14: 5. Orthonormal space concept
5.1 Orthonormal basis of transmitted signal
Suppose K = 3 time samples per transmitted signal X and per received signal Y respectively of a 3 x 3 channel transmission system were observed.
In figure 6, N = 3 transmitted signals and M = 3 received signals, the format of the unknown channel transfer matrix Wc would be 3 x 3. Assume that all signals are real valued and the transmitted signals and received signals are observed as signal matrices.
Then we need the orthonormal basis matrix Ux to solve for an estimated channel transfer matrix Wc.
It is easier to calculate the orthonormal base matrix Ux of a square matrix; therefore in the next section we estimate the channel model by calculating first the orthonormal basis matrix Ux of a simple 2 x 2 MIMO system and then proceed to a more complex 3 x 3 MIMO system.

## Slide 15: 5. Orthonormal space concept
5.2 Orthonormal basis Ux and transfer channel Wc estimation
5.2.1 A 2x2 MIMO system orthonormal base and channel estimation
To demonstrate the steps in subchapter 4.2, we will have a numerical example to explain how to generate the orthonormal basis Ux of a full rank square matrix using linearly independent transmitted signals in X.
The Gram-Schmidt procedure will be used in the decomposition of the transmitted signal X. The equation to decomposed in our calculation is of the form
In equation (5.2.1) the transmitted signal X is divided into two components, Ux the orthonormal basis and R the upper triangular matrixes.
The upper triangular matrix R is calculated by first finding the inverse of the orthonormal basis matrix Ux and multiplying it with the transmitted signal X.
However, the upper triangular matrix R is not needed in our analysis.

## Slide 17: 6. Generalized Fourier coefficients of X and Y
6.1 Generalized Fourier coefficients estimation (square case)
Generalized Fourier coefficients mean coefficients of any orthogonal set of functions over which a signal is split up.
Those functions are for example column vectors of the orthonormal bases Ux matrices in equation (5.3.3) and equation (5.4.6).
The generalized Fourier coefficients of the transmitted signal Wx tell how much each column signal of the transmitted signal X contains each orthogonal column components in the orthonormal base Ux.

## Slide 19: 7. Transfer channel estimation Wc
7.1 Channel estimation (square case)